## Slide 1
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
01 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
● HARDWARE & SOFTWARE INTEGRATED MATRIX
PROJECT A.U.R.A.
Autonomous Universal Rescue & Analysis Node
Subterranean Cavity Mapping, Multi-Modal Life Finding, Bio-Scent VOC Detection & Zero-Fake Cloud AI Triage for Frontline Disaster Search-and-Rescue.
PROBLEM STATEMENT ID
SIH1566 (Disaster Management & Robotics)
LEAD INSTITUTION
Panimalar Engineering College (Autonomous)
ENGINEERING TEAM
Team AntiGravity (6-Member Multi-Disciplinary)

## Slide 2
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
02 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
OPERATIONAL CONTEXT & THE 72-HOUR GOLDEN WINDOW
Overcoming Severe Physical Barriers in Post-Earthquake & Structural Collapse Search Operations
01. The Suffocation Clock
Trapped survivors endure concrete dust inhalation, toxic gas accumulation, hypothermia, and shock. Survival probability drops exponentially after the first 72 hours.
02. Optical / Thermal Drone Blindness
Aerial drones and thermal imaging cameras are completely blocked by dense, multi-layer reinforced concrete slabs and masonry rubble.
03. Wireless & RF Signal Attenuation
Radio communications, cellular signals, and Wi-Fi transmissions are heavily attenuated and dead beneath meters of twisted structural rebar.
04. Peril of Unassisted Blind Excavation
Excavating blindly with heavy hydraulic machinery destabilizes delicate void arches, crushing buried victims beneath fatal secondary cave-ins.
🚨 Critical Insight: 80% of preventable disaster fatalities occur due to delayed sub-surface victim localization during the Golden Window.

## Slide 3
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
03 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
THE PROPOSED SOLUTION — PROJECT A.U.R.A.
A Ruggedized, Rapidly-Deployable Multi-Modal Subterranean Penetrative Sensing Matrix
PILLAR 01
Multi-Physics Sensing Array
• Contact Seismic Geophone: Detects micro-impact distress knocks. • Acoustic Frequency Filter: Isolates human vocalizations. • Microwave Doppler Radar: Senses void chest flutter & motion. • MQ-135 Bio-Scent Sensor: Identifies metabolic breath VOCs.
PILLAR 02
Deterministic 500Hz Real-Time DSP
• ESP32 Core 1 Dedicated Pipeline. • Sub-millisecond interrupt envelope extraction. • Separates rhythmic human survivor taps from surface diesel generator noise. • Pure analog-to-digital physics with zero synthetic floors.
PILLAR 03
Neural Edge-to-Cloud AI Triage
• ESP32 Core 0 Async Web Server with Full CORS. • Streams live multi-transducer telemetry into Google Gemini Flash 1.5. • Generates instant surgical excavation azimuths (e.g. 320° NNW). • Delivers real-time spoken briefing to frontline rescue commanders.

## Slide 4
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
04 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
TACTICAL HARDWARE ENGINE & PINOUT MATRIX
ESP32-WROOM-32 Dual-Core Architecture (Core 0: Async WebServer & AI | Core 1: 500Hz DSP)
Component | Module Model | ESP32 Pin Mapping | Tactical Rescue Function
Central Node | ESP32-WROOM-32 | USB / 5V VIN & GND | Dual-Core 240MHz FreeRTOS Sensor & Comms Processing
Seismic Geophone | Piezo Ceramic Transducer | GPIO 35 (Analog ADC1) | Subterranean micro-impact tap counting (10Hz–250Hz)
Acoustic Listening Array | High-Sensitivity Mic | GPIO 32 (Analog ADC1) | Real-time dB acoustic spectrum (whispers, calls, shouts)
Microwave Doppler Radar | RCWL-0516 Radar | GPIO 33 (Digital IN) | Debris-penetrating chest flutter & micro-movement
Bio-Scent Gas Sensor | MQ-135 Sensor Array | GPIO 34 (Analog ADC1) | Human metabolic breath VOCs, NH3, and toxic air PPM
Structural IMU | MPU-6050 6-Axis | SDA: 21 / SCL: 22 (I2C) | Debris micro-jerk, tilt angle, and collapse risk monitoring
Tactical OLED Display | SSD1306 128x64 | SDA: 21 / SCL: 22 (0x3C) | 8-Slide animated live telemetry carousel for field operators

## Slide 5
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
05 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
SUBTERRANEAN THEATRE C2 DASHBOARD (REACT 19 + TYPESCRIPT)
Low-Latency Tactical Command Grid Designed for Ruggedized Field Tablets
FEATURE 01
Subterranean Theatre Topographic Radar
• Live strata depth slice visualizer with GPS lock to disaster deployment sector. • Precision GPS Anchor: Small Pond, Nehru Street (12.9676° N, 79.9462° E). • Interactive satellite navigation modal with Google Maps & OpenStreetMap overlays.
FEATURE 02
Fault-Tolerant Last Active Fix
• Offline GPS memory cache guarantees operational continuity during deep-rubble blackouts. • Preserves the exact last verified survivor coordinates. • Eliminates spatial drift even if wireless probe link is momentarily severed.
FEATURE 03
Real-Time Telemetry & Voice Orb
• 300ms live polling stream with Private Network Access (CORS). • Micro-audio oscilloscope & dynamic VOC bio-scent meters. • AURA Voice Orb: Hands-free tactical voice assistant delivering synthesized briefings to field commanders.

## Slide 6
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
06 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
EDGE-TO-CLOUD AI REASONING (ZERO FAKE TELEMETRY)
100% Physics-Driven Multi-Modal Sensor Ingestion — No Synthetic Floors or Scripted Data
AUTONOMOUS AI INFERENCE PIPELINE
Physical ADC Transducer Voltages ➔ Core 1 500Hz DSP Peak & Energy Extraction ➔ Core 0 JSON Telemetry Payload ➔ Google Gemini Flash 1.5 Cloud Inference
OUTPUT DIRECTIVE 01
Surgical Excavation Vector
Computes precise azimuth excavation angles (e.g. 320° NNW) to reach void pockets without destabilizing rubble arches.
OUTPUT DIRECTIVE 02
Sub-Surface Depth Estimation
Triangulates acoustic attenuation and seismic impulse wave speed to estimate victim burial depth (e.g. 2.4 meters ± 0.2m).
OUTPUT DIRECTIVE 03
Structural Integrity Triage
Classifies immediate collapse risk (NOMINAL / ALERT / CRITICAL) using real-time MPU-6050 jerk metrics and VOC levels.

## Slide 7
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
07 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
BENCHMARKING AGAINST EXISTING SEARCH TECHNOLOGIES
High-Performance Life Finding at 1/300th the Cost of Imported Foreign Equipment
Evaluation Metric | Thermal Drones | Search & Rescue K9s | Foreign Geophones (Delsar) | Project A.U.R.A.
Sub-Surface Penetration | 0m (Surface Only) | Scent Only (Wind-dependent) | Acoustic Only (Single-mode) | Multi-Modal (Seismic + Radar + Audio + Gas)
System Unit Cost | Rs. 8,00,000+ | High Training & Upkeep | Rs. 12,00,000 - 15,00,000 | < Rs. 3,500 ($42 USD)
Deployment Time | 15 - 20 mins setup | Rest breaks required | 10 mins calibration | < 15 Seconds (Instant On)
AI Triage Integration | None | None | None | Google Gemini Flash 1.5 Built-In
Local Visual Carousel | None | None | Analog Needle Gauge | 8-Slide OLED Screen Onboard

## Slide 8
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
08 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
PRODUCTION FEASIBILITY & NATIONAL SCALE ROADMAP
Sub-Rs. 3,500 BOM Economics Enabling Ubiquitous Deployment Across Indian Emergency Services
BILL OF MATERIALS (BOM) & COST ADVANTAGE
Total unit production cost < Rs. 3,500 INR (~$42 USD). Enables every local fire station, SDRF battalion, and NDRF quick-response unit to be equipped with multiple deployable probe nodes.
MILESTONE 01
Phase 1: Immediate Field Deployment (TRL-7)
• Standalone probe nodes with Wi-Fi / Hotspot C2 field tablets. • Tested with 500Hz DSP tap extraction & Google Gemini AI. • Ready for pilot trials at local emergency stations.
MILESTONE 02
Phase 2: Mesh Swarm Networking (Q2 2026)
• ESP-NOW LoRa Mesh multi-node swarm arrays. • Multi-acre coverage across massive disaster collapse zones. • Synchronized seismic trilateration for sub-meter 3D accuracy.
MILESTONE 03
Phase 3: Autonomous Rover Integration (Q4 2026)
• Micro-crawler robotic payload integration for deep void entry. • Tethered drone drop deployment for inaccessible rubble peaks. • Centralized National Disaster C2 Cloud Dashboard.

## Slide 9
SMART INDIA HACKATHON 2026 • MINISTRY OF HOME AFFAIRS (MHA) / NDRF • PS ID: SIH1566
09 / 09
PROJECT A.U.R.A. | Team AntiGravity | Panimalar Engineering College (Autonomous)
CORE ENGINEERING TEAM & LIVE SYSTEM DEMO
Panimalar Engineering College (Autonomous) • Motto: "Engineered for the Unseen. Built for the Golden Hour."
Jaffer Rilwaan V
LEAD SYSTEMS ARCHITECT
Full-Stack C2 Platform, Neural AI Integration & Telemetry Pipeline
Hannah Blessy J
HARDWARE & SENSOR LEAD
Piezoelectric Transducer Arrays & Bio-Scent VOC Hardware
Kathiravan S
TELEMETRY & CLOUD ENGINEER
Edge-to-Cloud Protocols & Resilient Networking
Kingston J
FIRMWARE & SIGNAL SPECIALIST
Dual-Core FreeRTOS & 500Hz DSP Filtering
Giridhar K
UI/UX & TACTICAL OPS LEAD
High-Contrast Tactical C2 HUD & Responder Experience
Nithyashree V
EMBEDDED POWER & QA LEAD
Energy Regulation, Battery Management & Sub-Surface QA Testing
🎯 READY FOR LIVE SYSTEM DEMONSTRATION | GitHub: github.com/jafferrilwaan-png/A.U.R.A-System